## Slide 1
John & Francisco Update:
FHEW <-> CKKS Scheme Switching
John & Francisco
FHE Hardware Accelerator
ECE Department

## Slide 2: Introduction
Evaluating timing of specific scheme switching steps for bi-directional changes from CKKS and FHEW
Discovered all of the code that drives all of the scheme switching capabilities to allow for profiling and datapath analysis
Found specific steps in CKKS->FHEW and FHEW->CKKS where it becomes costly to operate

## Slide 3: CKKS->FHEW I/O
EvalCKKStoFHEW
  Inputs:
    CKKS Ciphertext to switch | ciphertext
    # of coefficients to extract from CKKS ciphertexts (if 0, it defaults to # of slots) | numCtxts
  Outputs:
    Vector of LWE ciphertexts of length the number numCtxts

## Slide 4: CKKS->FHEW Case 1: Pipeline Time
Homomorphic Decoding: 15.0562ms
Modulus Switch: 1.4175ms
Key Switching: 1.1566ms
Extract LWE Ciphertexts: 0.1403ms
Modulus Switch: 0.0477ms
Total: 17.818

## Slide 5: FHEW->CKKS I/O
EvalCKKStoFHEW
  Inputs:
    FHEW/LWE ciphertexts to switch | LWECiphertexts to switch
    Number of values to encrypt from the LWE ciphertexts in the new CKKS ciphertext| numCtxts
    Number of slots to use in the encoding in the new CKKS/RLWE ciphertext | numSlots
    Plaintext modulus to use the decide post scaling, by default p = 4 | p
    Plaintext space of the resulting messages | pmin and pmax
  Outputs:
    CKKS ciphertext encryption in its slots the messages in the LWE ciphertexts

## Slide 6: FHEW->CKKS Case 1: Pipeline Time
Form Matrix & Vector from LWE Ciphertext: 0.0351ms
1st Homomorphic Linear Transform: 282.962ms
2nd Homomorphic Linear Transform: 6.6713ms
Do the modulus reduction homomorphically: 496.314ms
Post Process Ciphertext: 45.8854ms
Total: 831.833

## Slide 7: FHEW->CKKS: Next Steps
Understand why certain stages take longer than others by further analyzing code
  Homomorphic Decoding
  1st Homomorphic Linear Transform
  Modulus Reduction (Homomorphically)
Formulate a naive data path for the scheme switching for CKKS<->FHEW
Create RTL code structure based scheme switching datapath

## Slide 8
Thank you!